## Slide 1: Automatic Dam Shutter Controlling System
Group-01
  1706066
  1706073
  1706079
  1706080
  1706090
Presenting ID: 1706079

## Slide 2
What is Dam?
A dam is a barrier that stops or restricts the flow of surface water or underground streams.
Reservoirs created by dams not only suppress floods but also provide water for activities such as irrigation, human consumption, industrial use, aquaculture, and navigability.
Dams generally serve the primary purpose of retaining water, while other structures such as floodgates or levees are used to manage or prevent water flow into specific land regions.

## Slide 3
Components

## Slide 4: Components List
Self Made Linear Actuator
i) DC Motor
ii) Screw
Two acrylic box joined and a hole inside
Acrylic Shutter / dam
Arduino UNO
Sonar
Motor Driver ( LM 298)
DC Supply

## Slide 5
Construction of Linear Actuator
Presenting ID: 1706080

## Slide 6
Construction of Linear Actuator
The basic working principle of electric linear actuators is to convert the rotary motion into a linear motion. This conversion of motion is done with the help of a gearbox and a lead screw. These are the two most important electric linear actuator parts.

## Slide 7
This the Linear Actuator we made

## Slide 8
Working Principle
Presenting ID: 1706073

## Slide 9
Dam Water
1) Water height of the dam is minimum 10 cm to open the shutter and 17 m to close the shutter

## Slide 10
Dam Water
Sonar
1) Water height of the dam is minimum xxx to open the shutter and xxx m to close the shutter
2)Sonar will measure the water level and send it to arduino

## Slide 11
Dam Water
Arduino
Sonar
2)Sonar will measure the water level and send it to arduino
3) In Arduino code maximum, minimum water level
is provided to open or close the gate and then determining the polarity of voltage across the Actuator

## Slide 12
Dam Water
Arduino
Sonar
3) In Arduino code maximum, minimum water level
is provided to open or close the gate and then determining the polarity of voltage across the Actuator
Linear
Actuator
4) Motor will start to rotate after getting proper voltage . We have used a motor driver to ensure
best performance from actuator

## Slide 13
Dam Water
Arduino
Sonar
Dam open/close
Linear
Actuator
4) Motor will start to rotate after getting proper voltage . We have used a motor driver to ensure
best performance from actuator
5) If water crosses the maximum height level dam will be opened and when water level decreases to certain level dam will be closed

## Slide 14
Our Setup
Presenting ID: 1706090

## Slide 15
This is the full set up

## Slide 16
SONAR

## Slide 17
Motor Driver

## Slide 18
Arduino

## Slide 19
Circuit

## Slide 20
Dam Gate Controlled by Linear Actuator

## Slide 21: Importance of water dam
Controlling Flood
Storing Water
Generating Electricity